ITEM NO.

STEAM JACKETED KETTLE

KGL-60-T

(  ) REQUIRED

- Furnish (  ) each gas, self-contained tilting kettle model number KGL-60-T as manufactured by Cleveland.

- High efficiency Power Burner Heating System (62% to 65% efficiency)

- Fast Heat-up and Recovery Time, 140M BTU’s on 40-gallon models, 190M BTU’s on 60 gallon and larger

- Insulated Heat Exchanger

- Automatic Hot Surface Ignition System

- Steam Jacket permanently filled with treated, distilled water. Venting and/or refilling not required.

- Accurate, consistant solid state temperature controls - less than ±1°C variance (ideal for simmering). Operating temperature range from 145° - 260°F (63°C - 127°C)

- Standard Control Panel includes LED indicator for heat cycle, LED indicator for low water

- Power ON/OFF Dial with 1-10 Temperature Dial Setting easyDial Control Panel (optional) includes: Adjustable Temperature Control (C&F), 99 Minute Adjustable, Timer Setting, 3 Cooking Models, Cook/Simmer, Cook/On, Cook Off, 6-Built in Self Diagnostics & Display Readout

- Front mounted combination Pressure/Vacuum Gauge

- Type 316 Stainless Steel with #4 finish on kettle

- Tilt Mechanism of roller bearings and case-hardened self-locking worm and segment gear

- Support Legs with level adjustable feet, flanged for floor bolting

- Large pouring lip for easier, faster, pouring.  Heavy-duty Rolled Rim design provides strong reinforcement, prevents damages from abuse

- 50 psi Steam Jacket Rating and Safety Valve

- Standard voltage is 115 volts, 60 Hz, single-phase, supplied with cord and plug

- Standard for natural gas operation

- Provide the unit with the following accessories:

- Unit to be AGA, CE, CSA, ASME and NSF approved.

- Provide manufacturer's (1) year parts and labor warranty. Extended warranty, not to exceed 36 months from date of installation (K12 schools only).