ITEM NO.

TILTING SKILLET

SEL-40-T1

(   ) REQUIRED

- Furnish (  ) each electric, manual, 40 gallon tilting skillet model number SEL-40-T1 as manufactured by Cleveland.

- Open base design for easy cleaning and maintenance.

- 5/8" Stainless Steel Bead Blasted cooking surface prevents warping and keeps food from sticking.

- Durable 12-gauge, 304 Stainless Steel pan construction. 5/8˝(16mm) mild steel-clad bottom plus a 1/16˝ (1.6mm). Stainless Steel plate for even temperature distribution.

- Low 35" rim height for easy operation and cleaning.

- Splash Proof Controls and construction.

- Easy-to-turn manual hand tilt with enclosed permanently lubricated gearbox. Optional power tilt with manual override available.

- Gallon/Liter Markings and Vented Spring Assist Cover standard.

- Available with Optional 2" Tangent Draw-Off Valve.

- 10° Cooking Feature. Tilt unit up to 10° without the power being turned off.

- Adjustable, Electronic Thermostat accurately controls temperature from 100° to 450°F.

- Standard Voltages 208-240, single and three phase.

- Spring-Assist Cover with full width handle and vent.

- Adjustable Solid-State Thermostat accurately controls temperature

- from 140°F to 425°F

- Standard Control Panel includes: Temperature Control Dial, LED ON Indicator Light, Main Power, Switch with Standard and High Power Settings.

- easyDial Control Panel (optional) includes: Selector Dial with LED Ring, Large Display Screen, Three Cooking Modes, Built-In Self-Diagnostics and Display, Temperature Select Button, Timer Set Button (Hrs/Min), Settings Button, Main Power Button, Probe Connection Port, LED Indicator Lights for Heat-ON, Product Probe, Temperature, Time, Settings, Self-Diagnostics, Ignition Failure, Std and High Power Setting.

- Provide the unit with the following accessories:

- Unit to be UL, CSA, CE, and NSF approved.

- Provide manufacturer's (1) year parts and labor warranty.  Extended warranty, not to exceed 36 months from date of installation (K12 schools only).