ITEM NO.

TILTING SKILLET

SEL-40-TR

(   ) REQUIRED

- Furnish (  ) each electric powered, electric tilt, 40 gallon tilting skillet model number SEL-40-TR as manufactured by Cleveland.

- Space-Saving Design- No Clearance Required at rear or sides (optional Faucet and Console requires 4 1/2" on one side)

- All Stainless-Steel Construction for durability and easy cleaning

- Adjustable, Electronic Thermostat controls temperature from 100°F to 425°F

- High Efficiency Heating System with even heat distribution – 14 kW's for 30-gallon models, 18 kW's for 40 gallon models

- Fast Heat-Up and Recovery Time-Preheats in 15 minutes, full capacity from cold to boiling in 60 minutes

- Spring Assist Cover with Adjustable Vent and Full Width Handle

- On/Off Switch, Thermostat Knob and Pilots, recessed to avoid breakage

- Four Stainless Steel, Level adjustable feet, rear flanged for bolting

- Serviceable from the front of the unit

- Two Pilot Lights; Green = Power on, Amber = Temperature Cycling

- Meets IPX6 Water Rating Requirements

- High Limit Safety Device set at 450°F (232°C)

- Anti-Splash Pouring Lip

- Provide the unit with the following accessories:

- Unit to be UL, CSA, CE and NSF approved.

- Provide manufacturer's (1) year parts and labor warranty. Extended warranty, not to exceed 36 months from date of installation (K12 schools only).