ITEM NO.

TILTING SKILLET

SGL-40-TR

(   ) REQUIRED

- Furnish (  ) each gas powered, electric tilt, 40 gallon tilting skillet model number SGL-40-TR as manufactured by Cleveland.

- Adjustable, Electronic Thermostat controls temperature from 100°F to 425°F

- High Efficiency Heating System with even heat distribution

- Electronic Spark Ignition (ESS)

- Fast Heat-Up and Recovery Time-Preheats in 11 minutes, full capacity from cold to boiling in 60 minutes

- Spring Assist Cover with Adjustable Vent and Full Width Handle

- On/Off Switch, Thermostat Knob and Pilots, recessed to avoid breakage

- Four Stainless Steel, Level adjustable feet, rear flanged for bolting

- All Controls are serviceable from the front of the unit

- Two pilot lights; Green = Power on, Amber = Temperature Cycling

- Meets IPX6 Water Rating Requirements

- High Limit Safety Device set at 475°F (246°C)

- Anti-Splash Pouring Lip

- Supplied with Cord & Plug for 115-volt controls

- Provide the unit with the following accessories:

- Unit to be AGA, CSA, CE and NSF approved.

- Provide manufacturer's (1) year parts and labor warranty. Extended warranty, not to exceed 36 months from date of installation (K12 schools only).